## Slide 1: ILC Design Overview
Nick Walker (DESY/GDE)
GDE Internal Cost Review FNAL 13.11.12

## Slide 2: Contents
Requirements (from Physics and Detector)
Design evolution to the TDR baseline
Baseline 500 GeV Ecm Parameters
Approach to Site-Dependent Design Variants
ILC overview (intro to detail talks)
  RTML and bunch compressor
Emittance preservation (beam dynamics)
Low Ecm Running
Luminosity upgrade
TeV energy upgrade

## Slide 3: Requirements from ‘the customers’
Baseline:
  Energy range: 200 ≤ Ecm ≤ 500 GeV
  ∫Ldt ~ 500 fb-1 (in four years)
  Ability to make energy scans (about Ecm)
  DE/E ≤ 0.1%
    both pulse ‘jitter’ and bunch/train energy spread
  Electron polarisation ≥ 80%
  Support for two detectors
    push-pull
  Calibration at Z-pole (~90 GeV)
    but low lumi.
  Beamstrahlung ‘low’ (~few %)
Upgrades:
  Energy upgrade to ~ 1 TeV  important
  Not to exclude e-e- or gg collider options
  Polarised positrons ≥50%
  Giga-Z (Z factory with several 1033 cm-2s-1)
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/document.jsp?edmsid=*948205
focus of GDE design efforts
conceptual approach considered.
acknowledged but not considered in any detail

## Slide 4: ILC in a Nutshell
Damping Rings
Polarised electron source
Polarised positron source
Ring to Main Linac (RTML)
(inc. bunch compressors)
e- Main Linac
Beam Delivery System (BDS) & physics detectors
e+ Main Linac
Beam dump
not too scale

## Slide 5: Design Evolution: RDRTDR
2007 Reference Design Report and cost estimate
2008-2012 Technical Design Phase
Re-evaluation of baseline layout  updated design
Updated value estimate
RDR
SB2009

## Slide 6: Scope of Design Changes
31.5 MV/m average accelerating gradient including ±20% spread
Single tunnel for Main Linacs
Undulator-based e+ source relocation to end of e- Main Linac
  RDR: located at nominal 150 GeV point in elec. main linac
Reduced beam-power parameter set
  2625  1312 bunches per pulse (8.8  5.8mA)
  reduced klystron / modulator count (~30%)
  and…
6.43.2km circumference Damping Ring
Central region integration (general)
  RTML, sources and BDS integration

## Slide 7: ILC Published Parameters
Collision rate | Hz | 5 | 
Number of bunches |  | 1312 | 2625
Bunch population | ×1010 | 2 | 
Bunch separation | ns | 554 | 366
Pulse current | mA | 5.8 | 8.8
Beam pulse length | ms | 730 | 960
RMS bunch length | mm | 0.3 | 
Horizontal emittance | mm | 10 | 
Vertical emittance | nm | 35 | 
Electron polarisation | % | 80 | 
Positron polarisation | % | 30 | 
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass independent:
Luminosity Upgrade
Advantage of SCRF technology: long pulses

## Slide 8: ILC Published Parameters
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity | ×1034 cm-2s-1 | 0.50 | 0.59 | 0.75 | 0.93 | 1.8
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344
Notes: General observations:
Factor of 2 in L from enhancement – relatively large disruption parameter -> tight tolerances on collisions to IP (feedback)

## Slide 9: ILC Published Parameters
http://ilc-edmsdirect.desy.de/ilc-edmsdirect/item.jsp?edmsid=D00000000925325
Centre-of-mass dependent:
Centre-of-mass energy | GeV | 200 | 230 | 250 | 350 | 500
Electron RMS energy spread | % | 0.21 | 0.19 | 0.19 | 0.16 | 0.12
Positron RMS energy spread | % | 0.19 | 0.16 | 0.15 | 0.10 | 0.07
IP horizontal beta function | mm | 16 | 16 | 12 | 15 | 11
IP vertical beta function | mm | 0.48 | 0.48 | 0.48 | 0.48 | 0.48
IP RMS horizontal beam size | nm | 904 | 843 | 700 | 662 | 474
IP RMS veritcal beam size | nm | 9.3 | 8.6 | 8.3 | 7.0 | 5.9
Vertical disruption parameter |  | 20.4 | 20.4 | 23.5 | 21.1 | 24.6
Enhancement factor |  | 1.83 | 1.83 | 1.91 | 1.84 | 1.95
Geometric luminosity | ×1034 cm-2s-1 | 0.25 | 0.29 | 0.36 | 0.45 | 0.75
Luminosity | ×1034 cm-2s-1 | 0.50 | 0.59 | 0.75 | 0.93 | 1.8
% luminosity in top 1% DE/E |  | 92% | 90% | 84% | 79% | 63%
Average energy loss |  | 1% | 1% | 1% | 2% | 4%
Pairs / BX | ×103 | 41 | 50 | 70 | 89 | 139
Total pair energy / BX | TeV | 24 | 34 | 51 | 108 | 344
Focus of design (and cost!) effort

## Slide 10: ILC Footprint
Total site length (500 GeV CM) | 30.5 km
SCRF Main Linacs | 22.2 km
RTML (bunch compressors) | 2.8 km
Positron source | 1.1 km
BDS / IR | 4.5 km
Damping Rings (circumference) | 3.2 km
There are the SCRF main linacs….
… and there is everything else.

## Slide 11: Site-Dependent Designs
Top-level parameters
Accelerator layout
  lattice
  geometry
  parameters
  etc.
CFS requirements
  Central region (source, BDS, DR)
  RTML (bunch compressors)
Civil engineering solutions
  topography
  geology
Main linac layout
RF power distribution ( CFS)
cost effective tunnelling methods

## Slide 12: SCRF Linac Technology
1.3 GHz Nb 9-cellCavities | 16,024
Cryomodules | 1,855
SC quadrupole pkg | 673
10 MW MB Klystrons & modulators | 436 / 471 *
Approximately 20 years of R&D worldwide
 Mature technology
* site dependent
 Presentation by A. Yamamoto

## Slide 13: RF Power Source
Marx modulator
10MW MB Klystron
 Presentation by S. Fukuda
Adjustable local power distribution system

## Slide 14: Main Linac Parameters (500 GeV)
Average accelerating gradient | 31.5 (±20%) | MV/m
Cavity Q0 | 1010 | 
(Cavity qualification gradient | 35 (±20%) | MV/m)
Beam current | 5.8 | mA
Number of bunches per pulse | 1312 | 
Charge per bunch | 3.2 | nC
Bunch spacing | 554 | ns
Beam pulse length | 730 | ms
RF pulse length (incl. fill time) | 1.65 | ms
Efficiency (RFbeam) | 0.44 | 
Pulse repetition rate | 5 | Hz
Peak beam power per cavity | 190* | kW
* at 31.5 MV/m

## Slide 15: Site Dependence I: KCS
Klystron Cluster
Scheme
Novel system
35×10 MW MBK  350 MW
Feeds ~1 km of linac via over-moded circular WG (∅ 48 cm)
~8 MW ‘tapped-off’ every 26 cavities
Special Coxaxial Tap-Offs (CTO) used for both combining and splitting

## Slide 16: Site Dependence I: KCS
“Flat” topography site-dependent design
 Presentations by M. Ross and V. Kuchler

## Slide 17: Site Dependence II: DKS
“Mountainous” Topography site-dependent design
“Komoboko” tunnel
Reduced surface presence.
Horizontal access
Most infrastructure underground.
 Presentation by A. Enomoto

## Slide 18: Site Dependence II: DKS
accelerator cryomodules
Distributed
Klystron
Scheme
 presentations by M. Ross and S. Fukuda

## Slide 19: ILC in a Nutshell
Damping Rings
Polarised electron source
Polarised positron source
Ring to Main Linac (RTML)
(inc. bunch compressors)
e- Main Linac
Beam Delivery System (BDS) & physics detectors
e+ Main Linac
Beam dump
not too scale

## Slide 20: Ring To Main Linac (RTML)
5 GeV
15 GeV
5 GeV
5 GeV
15 GeV
5 GeV
(FoDo lattice)
bunch length: 6 mm
0.9 mm
0.3 mm
beam energy: 5 GeV
4.8 GeV
15 GeV
DE/E: 0.11%
1.42%
1.12%
÷6.7
÷3
R56 = -372 mm
R56 = -55 mm
DKS also used for flat topography site

## Slide 21: RTML / Bunch Compressor
Emittance preservation primary challenge
  fast ion instability in ~30km long return line
  stray time-varying fields (≤2 nT).
  spin rotation (solenoids  x-y coupling)
  RF and long bunch / large DE/E
     wakefields, coupler kicks, cavity tilt effects…
   beam based alignment
Tight requirements on phase/amplitude stability
  timing at IP  luminosity loss
  0.24° / 0.48° stability (correlated/uncorrelated)
  LLRF challenge

## Slide 22: Central Region
5.6 km region around IR
Systems:
  electron source
  positron source
  beam delivery system
  RTML (return line)
  IR (detector hall)
  damping rings
Complex and crowded area
Central Region
common tunnel

## Slide 23: Central Region
Example: Flat Topography
The central region beam tunnel remains a complex region.
Complete, detailed and integrated lattices are now available
Generic design used for geometry and generating component counts and CFS requirements.
CFS (particularly CE) solutions are site-dependent!
service tunnel

## Slide 24: Damping Rings
Circumference |  | 3.2 | km
Energy |  | 5 | GeV
RF frequency |  | 650 | MHz
Beam current |  | 390 | mA
Store time |  | 200 (100) | ms
Trans. damping time |  | 24 (13) | ms
Extracted emittance | x | 5.5 | mm
(normalised) | y | 20 | nm
No. cavities |  | 10 (12) | 
Total voltage |  | 14 (22) | MV
RF power / coupler |  | 176 (272) | kW
No.wiggler magnets |  | 54 | 
Total length wiggler |  | 113 | m
Wiggler field |  | 1.5 (2.2) | T
Beam power |  | 1.76 (2.38) | MW
Values in () are for 10-Hz mode
Many similarities to modern 3rd-generation light sources
 presentation by G. Dugan

## Slide 25: Positron Source (central region)
located at exit of electron Main Linac
147m SC helical undulator
driven by primary electron beam (150-250 GeV)
produces ~30 MeV photons
converted in thin target into e+e- pairs
not to scale!
yield = 1.5
 Presentation by W. Gai

## Slide 26: Polarised Electron Source
Laser-driven photo cathode (GaAs)
DC gun
Integrated into common tunnel with positron BDS
 Presentation by W. Gai

## Slide 27: BDS and MDI
e- BDS
e+ source
electron Beam Delivery System
 Presentation by K. Buesser
Geometry ready for TeV upgrade

## Slide 28: IR region (Final Doublet)
FD arrangement for push pull
  different L*
  ILD 4.5m, SiD 3.5m
Short FD for low Ecm
  Reduced bx*
    increased collimation depth
  “universal” FD
    avoid the need to exchange FD
    conceptual - requires study
Many integration issues remain
  requires engineering studies beyond TDR
  No apparent show stoppers
BNL prototype of self shielded quad
 Presentation by K. Buesser
Notes: Short FD effectively increases collimation depth (SR fan from FD). Universal FD (to prevent having to exchange cryostats) still requires proof of principle design.
Still many integration issues for IR/MDI. Requires engineering studies (beyond TDR).

## Slide 29: MDI (Detector Hall)
Flat-topography detector hall concept
 Presentation by K. Buesser
Notes: Should add mountain 3D graphic

## Slide 30: MDI (Detector Hall)
Mountainous-topography detector hall concept
 Presentation by K. Buesser
Notes: Should add mountain 3D graphic

## Slide 31: Central Region Integration
e- BDS
e- BDS muon shield
e+ main beam dump
detector
RTML return line
e+ source
Damping Rings
3D CAD has been used to developed beamline layouts and tunnel requirements.
Complete model of ILC available.

## Slide 32: Where are we?
Requirements (from Physics and Detector)
Design evolution to the TDR baseline
Baseline 500 GeV Ecm Parameters
Approach to Site-Dependent Design Variants
ILC overview (intro to detail talks)
  RTML and bunch compressor
Emittance preservation (beam dynamics)
Low Ecm Running
Luminosity upgrade
TeV energy upgrade

## Slide 33: Emittance Preservation
Damping Ring: gey = 20nm
  ~30km RTML return line
  Turn around and spin rotation
  Bunch compressor (two-stages)
  Acceleration (10km main linac)
  Positron production (e- only)
  Beam delivery system (non-linear optics)
  Final Doublet and collision!
Budget 15 nm  gey = 35 nm at IP

## Slide 34: Emittance Budgets
 | Mean | 90% level
Damping ring extraction | 20 | 
RTML (Return line, turn-around, spin rotation) | +5.4 | 9.9
RTML (Bunch compressors) | +1.1 | 1.5
Main Linac | +4.5 | 8.8
End of Main Linac (total) | 31 | 37
BDS (budgeted) | +4 | 
IP (effective): | 35 | >40
Results of extensive simulations
(over 10 years)
Standard alignment (survey) errors assumed
Several beam-based alignment techniques studied (most notably DFS)
‘Realistic’ simulation (including wakefields, non-linear fields etc.)
Tuning algorithms (dispersive closed bumps, final focus tuning etc.)
Dynamic errors included (ground motion, vibration, beam-based feedback etc.)
 35nm @ IP looks OK on average (in simulation!)

## Slide 35: Low Ecm Running (<300 GeV)
Positron production (yield) drops with <150 GeV
Low Ecm running (≤250 GeV)  10Hz mode
Alternate pulses for e+ production:
  150 GeV e- pulse to generate positrons
  Ecm/2 e- pulse for luminosity
Ramifications:
  100ms store time in DR  shorter damping times
  Need to dump 150 GeV production pulse after undulator (new beamline, pulsed-magnet system)
  Pulsed trajectory-correction system before undulator for 150 GeV production beam.
Electron Main Linac requires no modification
  Installed AC power sufficient for ~½ energy operation at 10Hz.

## Slide 36: Luminosity Upgrade
Concept: increase nb from 1312 → 2625
  Reduce linac bunch spacing 554 ns → 336 ns
  Increase pulse current 5.8 → 8.8 mA
  Increase number of klystrons by ~50%
Doubles beam power  ×2 L (3.6×1034cm-2s-1)
Damping ring:
  Electron ring doubles current (389mA  778mA)
  Positron ring: possible 2nd (stacked) ring (e-cloud limit)
AC power: 161 MW  204 MW (est.)
  AC power increased by ×1.5
  shorter fill time and longer beam pulse results in higher RF-beam efficiency (44%  61%)

## Slide 37: Luminosity Upgrade
Adding klystrons (and modulators)
Flat Topography (KCS)
MountainTopography (DKS)
KCS Building
Damping Ring:

## Slide 38: TeV Upgrade
2.2 km
1.3 km
10.8 km
1.1 km
BDS
Main Linac
e+ src
bunch comp.
<26 km ?
(site length <52 km ?)
Main Linac
<Gcavity> = 31.5 MV/m
Geff ≈ 22.7 MV/m
(fill fact. = 0.72)
IP
central region
<10.8 km ?
Snowmass 2005 baseline recommendation for TeV upgrade:
Gcavity = 36 MV/m ⇒ 9.6 km
(VT ≥ 40 MV/m)
Based on use of low-loss or re-entrant cavity shapes
Assume Higher Gradient

## Slide 39: TeV upgrade: Construction Scenario
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
start civil construction
500GeV operations
500GeV operations
Installation/upgrade shutdown
civil construction + installation
final installation/connection
removal/relocation of BC
Removal of turnaround etc.
Installation of addition magnets etc.
Commissioning / operation at 1TeV
Notes: An obvious possible approach to minimizing downtime for physics.
Assume something like a total of 5 year construction with perhaps 12-18 months with no physics??

## Slide 40: TeV Parameters (2 sets)
low and high beamstrahlung
horizontal focusing main difference
shorter bunch length (within BC range)
PAC constrained ≤300 MW

## Slide 41: Detailed Presentations
SCRF Tech: Cavities and Cryomodules | A. Yamamoto
afternoon: | 
Main linac layouts (incl. design variants) | M. Ross
RF power generation / distribution | S. Fukuda
Electron and positron sources | W. Gai
Damping Rings | G. Dugan
Beam delivery system and MDI | K. Buesser
CFS | V. Kuchler A. Enomoto